BAT6

---
Welcome
Raphael Frey

---
Model and Regulation
Reto Freivogel

---
Our Model (Temperature)

---
Our Model (Irradiation)

---
Regulation Algorithm

---
Hardware Implementation
1.5V
Vref
dsPIC33
DAC
ADC
Buck
(LT3741)
ADC
DAC
Set Voltage
Measure Current
Set Current
Measure Voltage
[Speaker Notes: → the main parts of the regulation → Measure V + I at all times → If we take a look at a typical IV curve we see there is a part where the voltage is relatively constant → Operate in constant voltage mode → or constant current → to improve accuracy]

---
Hardware
Alex Murray

---
Full Use of Today's Technologies
[Speaker Notes: → Full use of modern fabrication technologies → As close as possible to behaviour of a possibly mass produced product → SMD, tiny ICs, QFN → Fabricated PCB → Reflow soldering to manufacture → (explain shit) → Unfortunately,]

---
The Issue
- MOSFETs are fine
- Inductor is fine
- No significant heat dissipation
- Transients?
[Speaker Notes: → This is a block diagram of… → After lots of analysing and measuring… → concluded high side driver broken → This happened twice → replaced regulator, reduced voltage, same thing → (next slide)]

---
Trace Lengths Are Fairly Long
Resistors
>2cm
Absolute Maximum
actual
Expected Maximum
Ideal
With resistors
[Speaker Notes: → View of our printed circuit board → If we take a look at traces… → Inductance of traces isn't considered in simulation → Traces can be modelled & simulated → This is what we get when we do that → 40V/28V red lines → Yellow = ideal → Blue = simulation with traces → Ringing, transients overshooting by 12V → How do we fix? → Resistors in series (3.3 Ohm)]

---
Solutions
- Series Resistors
- Place LT3741 closer to MOSFETs
Minimise
Distance
[Speaker Notes: Second Iteration of the design → Decrease distance between regulator and MOSFETs]

---
Demonstration
Raphael Frey

---
Conclusions / TODO
- Fix Problems
- Test/Verify functionality

---
Project Repository
Gource Time-lapse
github.com/thecomet93/bat6
http://tinyurl.com/fhbat6
Questions?

---
Thank You!

---
Thank You!

---
Threshold